## Slide 1: Chapter 6: Network Layer
Introduction to Networks
Notes: Cisco Networking Academy program
Introduction to Networks
Chapter 6: Network Layer

## Slide 2: Chapter 6: Objectives
Students will be able to:
Explain how network layer protocols and services support communications across data networks.
Explain how routers enable end-to-end connectivity in a small to medium-sized business network.
Determine the appropriate device to route traffic in a small to medium-sized business network.
Configure a router with basic configurations.
Notes: 2

## Slide 3: Chapter 6
  6.1 Network Layer Protocols
  6.2 Routing
  6.3 Routers
  6.4 Configuring a Cisco Router
  6.5 Summary
Notes: Chapter 6 Sections

## Slide 4: Network Layer Network Layer
Notes: Section 6.0

## Slide 5: Network Layer Protocols Network Layer in Communication
Notes: Section 6.1.1

## Slide 6: Network Layer in Communication The Network Layer
End to End Transport processes
Addressing end devices
Encapsulation
Routing
De-encapsulating
Notes: Section 6.1.1.1

## Slide 7: Network Layer in Communication Network Layer Protocols
Common Network Layer Protocols
Internet Protocol version 4 (IPv4)
Internet Protocol version 6 (IPv6)
Legacy Network Layer Protocols
Novell Internetwork Packet Exchange (IPX)
AppleTalk
Connectionless Network Service (CLNS/DECNet)
Notes: Section 6.1.1.2

## Slide 8: Characteristics of the IP protocol Characteristics of IP
Notes: Section 6.1.2.1

## Slide 9: Characteristics of the IP protocol IP - Connectionless
Notes: Section 6.1.2.2

## Slide 10: Characteristics of the IP protocol IP – Best Effort Delivery
Notes: Section 6.1.2.3

## Slide 11: Characteristics of the IP protocol IP – Media Independent
Notes: Section 6.1.2.4

## Slide 12: IPv4 Packet Encapsulating IP
Notes: Section 6.1.2.5

## Slide 13: IPv4 Packet IPv4 Packet Header
Version, Differentiated Services (DS), Time-to-Live (TTL),Protocol, Source IP Address, Destination IP Address
Version | IP Header Length | Differentiated Services |  | Total Length |  |  | 
 |  | DSCP | ECN |  |  |  | 
Identification |  |  |  | Flag | Fragment Offset |  | 
Time To Live |  | Protocol |  | Header Checksum |  |  | 
Source IP Address |  |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  |  | 
Options (optional) |  |  |  |  |  |  | Padding
Byte 1
Byte 2
Byte 3
Byte 4
Notes: Section 6.1.3.2

## Slide 14: IPv4 Packet IPv4 Header Fields
Internet Header Length (IHL), Total Length, Header Checksum, Identification, Flags, Fragment Offset
Version | IP Header Length | Differentiated Services |  | Total Length |  |  | 
 |  | DSCP | ECN |  |  |  | 
Identification |  |  |  | Flag | Fragment Offset |  | 
Time To Live |  | Protocol |  | Header Checksum |  |  | 
Source IP Address |  |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  |  | 
Options (optional) |  |  |  |  |  |  | Padding
Byte 1
Byte 2
Byte 3
Byte 4
Notes: Section 6.1.3.3

## Slide 15: IPv4 Packet Sample IPv4 Headers
Notes: Section 6.1.3.4

## Slide 16: Network Layer in Communication Limitations of IPv4
IP Address depletion
Internet routing table expansion
Lack of end-to-end connectivity
Notes: Section 6.1.4.1

## Slide 17: Network Layer in Communication Introducing IPv6
Increased address space
Improved packet handling
Eliminates the need for NAT
Integrated security
4 billion IPv4 addresses 4,000,000,000
340 undecillion IPv6 addresses 340,000,000,000,000,000,000,000,000,000,000,000,000
Notes: Section 6.1.4.2

## Slide 18: IPv6 Packet Encapsulating IPv6
Notes: Section 6.1.4.3

## Slide 19: IPv6 Packet IPv6 Packet Header
Version | Traffic Class |  | Flow Label |  |  | 
Payload Length |  |  |  | Next Header | Hop Limit | 
Source IP Address |  |  |  |  |  | 
Destination IP Address |  |  |  |  |  | 
Byte 1
Byte 2
Byte 3
Byte 4
Notes: Section 6.1.4.4

## Slide 20: IPv6 Packet Sample IPv6 Header
Notes: Section 6.1.4.3

## Slide 21: Routing Host Routing Tables
Notes: Section 6.2.1

## Slide 22: Host Routing Tables Host Packet Forwarding Decision
Notes: Section 6.2.1.1

## Slide 23: Host Routing Tables Default Gateway
Hosts must maintain their own, local, routing table to ensure that network layer packets are directed to the correct destination network. The local table of the host typically contains:
Direct connection
Local network route
Local default route
R
Notes: Section 6.2.1.2

## Slide 24: Host Routing Tables IPv4 Host Routing Table
Notes: Section 6.2.1.3 6.2.1.4

## Slide 25: Host Routing Tables Sample IPv4 Host Routing Table
Notes: Section 6.2.1.5

## Slide 26: Host Routing Tables Sample IPv6 Host Routing Table
Notes: Section 6.2.1.6

## Slide 27: Router Routing Tables Router Packet Forwarding Decision
Notes: Section 6.2.2.1

## Slide 28: Router Routing Tables IPv4 Router Routing Table
R1#show ip route
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
D 10.1.1.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
D 10.1.2.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
192.168.10.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
L 192.168.10.1/32 is directly connected, GigabitEthernet0/0
192.168.11.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
L 192.168.11.1/32 is directly connected, GigabitEthernet0/1
209.165.200.0/24 is variably subnetted, 2 subnets, 3 masks
C 209.165.200.224/30 is directly connected, Serial0/0/0
L 209.165.200.225/32 is directly connected, Serial0/0/0
R1#
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: Section 6.2.2.2

## Slide 29: Router Routing Tables Directly Connected Routing Table Entries
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
L 192.168.10.1/32 is directly connected, GigabitEthernet0/0
A
B
C
A | Identifies how the network was learned by the router.
B | Identifies the destination network and how it is connected.
C | Identifies the interface on the router connected to the destination network.
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
64.100.0.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: Section 6.2.2.3

## Slide 30: Router Routing Tables Remote Network Routing Table Entries
D 10.1.1.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
A | Identifies how the network was learned by the router.
B | Identifies the destination network.
C | Identifies the administrative distance (trustworthiness) of the route source.
D | Identifies the metric to reach the remote network.
E | Identifies the next hop IP address to reach the remote network.
F | Identifies the amount of elapsed time since the network was discovered.
G | Identifies the outgoing interface on the router to reach the destination network.
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
64.100.0.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Notes: Section 6.2.2.4

## Slide 31: Router Routing Tables Next-Hop Address
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
64.100.0.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
R1#show ip route
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
10.0.0.0/8 is variably subnetted, 2 subnets, 2 masks
D 10.1.1.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
D 10.1.2.0/24 [90/2170112] via 209.165.200.226, 00:00:05, Serial0/0/0
192.168.10.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
L 192.168.10.1/32 is directly connected, GigabitEthernet0/0
192.168.11.0/24 is variably subnetted, 2 subnets, 3 masks
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
L 192.168.11.1/32 is directly connected, GigabitEthernet0/1
209.165.200.0/24 is variably subnetted, 2 subnets, 3 masks
C 209.165.200.224/30 is directly connected, Serial0/0/0
L 209.165.200.225/32 is directly connected, Serial0/0/0
R1#
Notes: Section 6.2.2.5

## Slide 32: Routers Anatomy of a Router
Notes: Section 6.3.1

## Slide 33: Anatomy of a Router A Router is a Computer
Notes: Section 6.3.1.1

## Slide 34: Anatomy of a Router Router CPU and OS
Notes: Section 6.3.1.2

## Slide 35: Anatomy of a Router Router Memory
Memory | Volatile / Non-Volatile | Stores
RAM | Volatile | Running IOS Running configuration file IP routing and ARP tables Packet buffer
ROM | Non-Volatile | Bootup instructions Basic diagnostic software Limited IOS
NVRAM | Non-Volatile | Startup configuration file
Flash | Non-Volatile | IOS Other system files
Notes: Section 6.3.1.3

## Slide 36: Anatomy of a Router Inside a Router
Notes: Section 6.3.1.4

## Slide 37: Anatomy of a Router Router Backplane
Two 4 GB flash card slots
Double-wide eHWIC slots
eHWIC 0
AUX
port
LAN
interfaces
USB
Ports
Console
USB Type B
Console RJ45
Notes: Section 6.3.1.5

## Slide 38: Anatomy of a Router Connecting to a Router
WAN
Interface
AUX
port
LAN
interfaces
Console
USB Type B
Console RJ45
Notes: Section 6.3.1.6

## Slide 39: Anatomy of a Router LAN and WAN Interfaces
Serial interfaces
LAN interfaces
Notes: Section 6.3.1.7

## Slide 40: Router Boot-up Cisco IOS
Notes: Section 6.3.2.1

## Slide 41: Router Boot-up Bootset Files
Notes: Section 6.3.2.2

## Slide 42: Router Boot-up Router Bootup Process
System Bootstrap, Version 15.0(1r)M15, RELEASE SOFTWARE (fc1)
Technical Support: http://www.cisco.com/techsupport
<output omitted>
Perform the POST and load the bootstrap program
Locate and load the Cisco IOS software
Locate and load the startup configuration file or enter setup mode
Notes: Section 6.3.2.3

## Slide 43: Router Boot-up Show Versions Output
Router# show version
Cisco IOS Software, C1900 Software (C1900-UNIVERSALK9-M), Version 15.2(4)M1, RELEASE SOFTWARE (fc1)
Technical Support: http://www.cisco.com/techsupport
Copyright (c) 1986-2012 by Cisco Systems, Inc.
Compiled Thu 26-Jul-12 19:34 by prod_rel_team
ROM: System Bootstrap, Version 15.0(1r)M15, RELEASE SOFTWARE (fc1)
Router uptime is 10 hours, 9 minutes
System returned to ROM by power-on
System image file is "flash0:c1900-universalk9-mz.SPA.152-4.M1.bin"
Last reload type: Normal Reload
Last reload reason: power-on
<Output omitted>
Cisco CISCO1941/K9 (revision 1.0) with 446464K/77824K bytes of memory.
Processor board ID FTX1636848Z
2 Gigabit Ethernet interfaces
2 Serial(sync/async) interfaces
1 terminal line
DRAM configuration is 64 bits wide with parity disabled.
255K bytes of non-volatile configuration memory.
250880K bytes of ATA System CompactFlash 0 (Read/Write)
<Output omitted>
Technology Package License Information for Module:'c1900'
-----------------------------------------------------------------
Technology Technology-package Technology-package
Current Type Next reboot
------------------------------------------------------------------
ipbase ipbasek9 Permanent ipbasek9
security None None None
data None None None
Configuration register is 0x2142 (will be 0x2102 at next reload)
Router#
Notes: Section 6.3.2.4

## Slide 44: Network Layer Configuring a Cisco Router
Notes: Section 6.4

## Slide 45: Configure Initial Settings Router Configuration Steps
Router> enable
Router# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)# hostname R1
R1(config)#
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
Router> en
Router# conf t
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)# ho R1
R2(config)#
OR
R1(config)# enable secret class
R1(config)#
R1(config)# line console 0
R1(config-line)# password cisco
R1(config-line)# login
R1(config-line)# exit
R1(config)#
R1(config)# line vty 0 4
R1(config-line)# password cisco
R1(config-line)# login
R1(config-line)# exit
R1(config)#
R1(config)# service password-encryption
R1(config)#
R1(config)# banner motd #
Enter TEXT message. End with the character '#'.
***********************************************
WARNING: Unauthorized access is prohibited!
***********************************************
#
R1(config)#
R1# copy running-config startup-config
Destination filename [startup-config]?
Building configuration...
[OK]
R1#
Notes: Section 6.4.1.1

## Slide 46: Configure Interfaces Configure LAN Interfaces
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
R1# conf t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)#
R1(config)# interface gigabitethernet 0/0
R1(config-if)# ip address 192.168.10.1 255.255.255.0
R1(config-if)# description Link to LAN-10
R1(config-if)# no shutdown
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0, changed state to up
R1(config-if)# exit
R1(config)#
R1(config)# int g0/1
R1(config-if)# ip add 192.168.11.1 255.255.255.0
R1(config-if)# des Link to LAN-11
R1(config-if)# no shut
%LINK-5-CHANGED: Interface GigabitEthernet0/1, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/1, changed state to up
R1(config-if)# exit
R1(config)#
Notes: Section 6.4.2.1

## Slide 47: Configure Interfaces Verify Interface Configuration
192.168.10.0/24
R2
192.168.11.0/24
10.1.1.0/24
10.1.2.0/24
209.165.200.224 /30
.226
.10
.10
.10
.10
.1
.1
.1
G0/1
.225
S0/0/0
G0/0
.1
R1
PC1
PC2
R1# show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 192.168.10.1 YES manual up up
GigabitEthernet0/1 192.168.11.1 YES manual up up
Serial0/0/0 209.165.200.225 YES manual up up
Serial0/0/1 unassigned YES NVRAM administratively down down
Vlan1 unassigned YES NVRAM administratively down down
R1#
R1# ping 209.165.200.226
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 209.165.200.226, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/2/9 ms
R1#
Notes: Section 6.4.2.2

## Slide 48: Configuring a Cisco Router Configuring the Default Gateway
Notes: Section 6.4.3

## Slide 49: Configuring the Default Gateway Default Gateway on a Host
192.168.10.0/24
192.168.11.0/24
G0/1
.1
.1
G0/0
R1
.10
PC1
.10
PC2
.10
PC4
.10
PC3
192.168.10.0/24
192.168.11.0/24
G0/1
.1
.1
G0/0
R1
.10
PC1
.11
PC2
.11
PC4
.10
PC3
Notes: Section 6.4.3.1

## Slide 50: Configuring the Default Gateway Default Gateway on a Switch
192.168.11.0/24
.1
G0/1
.1
G0/0
R1
192.168.10.0/24
.10
PC1
.11
PC2
S1#show running-config
Building configuration...
!
<output omitted>
service password-encryption
!
hostname S1
!
Interface Vlan1
ip address 192.168.10.50
!
ip default-gateway 192.168.10.1
<output omitted>
S1
S2
.50
If the default gateway were not configured on S1, response packets from S1 would not be able to reach the administrator at 192.168.11.10. The administrator would not be able to mange the device remotely.
Notes: Section 6.4.3.2

## Slide 51: Network Layer Summary
In this chapter, you learned:
The network layer, or OSI Layer 3, provides services to allow end devices to exchange data across the network.
The network layer uses four basic processes: IP addressing for end devices, encapsulation, routing, and de-encapsulation.
The Internet is largely based on IPv4, which is still the most widely-used network layer protocol.
An IPv4 packet contains the IP header and the payload.
The IPv6 simplified header offers several advantages over IPv4, including better routing efficiency, simplified extension headers, and capability for per-flow processing.
Notes: Section 1.5 & 1.5.1

## Slide 52: Network Layer Summary
In this chapter, you learned:
In addition to hierarchical addressing, the network layer is also responsible for routing.
Hosts require a local routing table to ensure that packets are directed to the correct destination network.
The local default route is the route to the default gateway.
The default gateway is the IP address of a router interface connected to the local network.
When a router, such as the default gateway, receives a packet, it examines the destination IP address to determine the destination network.
Notes: Section 1.5 & 1.5.1

## Slide 53: Network Layer Summary
In this chapter, you learned:
The routing table of a router stores information about directly-connected routes and remote routes to IP networks. If the router has an entry in its routing table for the destination network, the router forwards the packet. If no routing entry exists, the router may forward the packet to its own default route, if one is configured, or it will drop the packet.
Routing table entries can be configured manually on each router to provide static routing or the routers may communicate route information dynamically between each other using a routing protocol.
In order for routers to be reachable, the router interface must be configured.
Notes: Section 1.5 & 1.5.1