## Slide 1: Network Cards

## Slide 2: Objectives
1. Network Interface Cards (NIC) Basics
2. Choosing Network Adapters for Best Performance
3. Special-Purpose NICs
4. Driver Software

## Slide 3: Network Interface Cards (NIC) Basics
  1.1. From Parallel to Serial and Vice Versa
  1.2. Additional Functions of a NIC
  1.3. PC Buses
  1.4. Other PC Interfaces Used for Networking
  1.5. Principles of NIC Configuration
  1.6. Integrated NICs
  1.7. Making the Network Attachment

## Slide 4
For any computer, a network interface card (NIC) performs two crucial tasks
  Establishes and manages the computer’s network connection
  Translates digital computer data into signals (appropriate for the networking medium) for outgoing messages, and translates signals into digital computer data for incoming messages
NIC establishes a link between a computer and a network, and then manages that link

## Slide 5: From Parallel to Serial and Vice Versa
NICs also manage transformations in network data’s form
  The computer bus has series of parallel data lines
    Parallel transmission
For nearly all forms of networking media, signals traversing the media consist of a linear sequence of information that corresponds to a linear sequence of bits of data (serial transmission)
To redistribute serial data to parallel lines (and vice versa), one of the most important components on a NIC is memory, which acts as a buffer

## Slide 6
Bus width

## Slide 8: Additional Functions of a NIC
Creates, sends, and receives frames
  Frame: fundamental unit of data for network transmission and reception
Deals with frame-level errors and incomplete or unintelligible frame structures
Manages access to medium
Acts as gatekeeper (permits inbound communications aimed only at its computer (or broadcast) to pass through NIC and on to CPU)
  Each card has a unique MAC address in ROM
  Promiscuous mode disables gatekeeper functions

## Slide 9: PC Buses
When PCs were introduced, only a single bus design existed: a limited 8-bit bus
As technology evolved, other buses came along
  Peripheral Component Interconnect (PCI)
  PCI-X
  PCI Express
  PCMCIA cards
  Industry Standard Architecture (ISA)

## Slide 13: Other PC Interfaces Used for Networking
Although the following interface technologies don’t replace the buses in most typical PCs, they do offer other ways to attach computers to networks:
  Universal Serial Bus (USB)
    USB 1.0 can operate at up to 12 Mbps
    USB 2.0 can operate at up to 480 Mbps
  FireWire (also known as IEEE 1394)
    Can operate up to 400 Mbps
    IEEE 1394b supports transfer rates up to 3200 Mbps

## Slide 14: Principles of NIC Configuration
Microsoft introduced Plug and Play (PnP) architecture with Windows 95
  Defines a set of configuration protocols so that a computer can communicate with its peripherals during the power-on self test (POST) sequence and auto-negotiate a working configuration
NIC configuration involves modifying settings
  Interrupt request line (IRQ)
  Base I/O port
  Base memory address

## Slide 15: Integrated NICs
On-board NICs: Most PC motherboard and laptop computer manufacturers integrate the network interface directly on to the motherboard
  Might not meet a user’s needs
    Wrong media
    Wrong speed
    Wrong architecture
  Most on-board NICs are suitable for most users’ requirements

## Slide 16: Making the Network Attachment
NICs perform several vital roles to coordinate communications between computer and network
  Establishing a physical link to networking medium
  Generating signals that traverse networking medium
  Receiving incoming signals
  Implementing controls for when to transmit signals to or receive signals from the network medium
It is essential that you matching the adapter you choose with the medium it must attach to
Some NICs support multiple media types, and configuration is usually automatic or uses SW

## Slide 17: Choosing Network Adapters for Best Performance
The hardware-enhancement NIC options include:
  Direct Memory Access (DMA)
  Shared adapter memory
  Shared system memory
  Bus mastering
  RAM buffering
  On-board co-processors
  Various security options
  Traffic management (Quality of Service (QoS))
  Automatic link aggregation
  Improved fault tolerance
  Improved management features

## Slide 18
Increased performance features have payoffs for servers that might not apply to workstations
  The following is a checklist for purchasing NICs:
    Bus width—Higher is better
    Bus type—Use 64-bit PCI-X or PCIe for servers
    Memory transfer—Shared memory outpaces I/O or DMA
    Special features—Choose security, management, protocol-handling, and hot-plug capabilities
    Bus mastering—Important for servers
    Vendor factors—Look for quality, reliability, staying power, and reputation

## Slide 19: Special-Purpose NICs
  3.1. Wireless Adapters
  3.2. Remote Boot Adapters

## Slide 20
In addition to straightforward network adapters, several types of cards deliver specialized capabilities
  They include interfaces for wireless networks, as well as a feature for so-called diskless workstations (“thin clients”), which must access the network to load an OS when they boot
    These cards are said to support remote booting or remote initial program load

## Slide 21: Wireless Adapters
Wireless interfaces usually incorporate some or all of the following components:
  Indoor antenna and antenna cable
  Software to enable the adapter to work with a particular network environment
  Diagnostic software
  Installation software
Wireless NICs are commonly used with an access point to add wireless elements to an existing LAN
Select: speed, wireless standard, other (e.g., security)

## Slide 23: Remote Boot Adapters
The network must be the source of access to the programs needed to start a diskless workstation
  Some NICs include a chip socket for a special bit of circuitry called a Boot PROM, which is referred to as preboot execution environment (PXE) compliant
  Remote boot adapters offer several advantages
    Cost savings because no hard drive is required
    Improved reliability (hard drives are a common source of problems)
    Security is increased (no sensitive data can be stored on the computer)
    Virus attacks are useless

## Slide 24: Driver Software
  4.1. NIC Driver Configuration
  4.2. Wireless NIC Configuration

## Slide 25
Device driver: small, specialized program that represents a device to an OS and manages communications between the OS and NIC
Incorrect/poorly written drivers can have negative impact on performance or prevent PC from booting
Major vendor standards for drivers
  Network Device Interface Specification (NDIS)
  Win32 Driver Model (WDM)
  Open Data-link Interface (ODI)
Installing a driver for a NIC is usually easy

## Slide 27: NIC Driver Configuration

## Slide 29: Wireless NIC Configuration

## Slide 31: Summary
NICs supply the interface between a computer and the networking medium
  When sending data, a NIC reformats outgoing data from the parallel form that arrives through the computer’s bus to the serial form used over most media; to receive data, the process is reversed
NICs have options that must be set for an adapter to make a working network connection (usually PnP)
NIC’s edge connector must match the PC slot
Many motherboards have integrated NICs
Network adapters can have a profound effect on overall network performance

## Slide 32
When purchasing a network adapter, consider the following checklist: bus width, bus type, memory transfer, special features (such as security), bus mastering, and vendor factors (such as support)
When purchasing a wireless NIC, keep in mind the Wi-Fi standard you want to use
Driver software permits a NIC to communicate with a computer’s operating system
  NIC driver configuration can be auto-configured, or it might require setting some options