## Slide 1: Sending and receiving information among computers

## Slide 2: Objectives
Describe the basic components of a network
Explain the methods of data transmission, including types of signals, modulation, and choices among transmission modes
Differentiate among the various kinds of communications links and appreciate the need for protocols
Describe various network configurations
List the components, types, and protocols of a local area network
Appreciate the complexity of networking
Describe some examples of networking

## Slide 3
The technical and business community recognized the need to share information among com- puters. However, there were still a few hurdles that needed to be overcome before a computer network could be created.
The earliest PC network linked computers and a printer through an electronic switch. This posed less of a challenge than networking computers together since information flowed in one direction: from a computer to the electronic switch.

## Slide 4: Tech Talk Protocol:
A set of rules that determines the method that will be used to do a task, such as to send and receive information.
expected response.

## Slide 6: Asynchronous communication:
Divides information into pieces and transmits each piece separately to the remote computer. The remote computer acknowledges each piece before the next piece is sent. The pieces are reassembled at the destination.

## Slide 7: Tech Talk File server:
A dedicated computer on a computer network that is used to store flies that are shared among computers connected to the network.

## Slide 8: Tech Talk Contention:
When two or more computers attempt to access a network resource at the same time.
New technology had to be developed to meet these challenges. Technicians focused on three components: a network circuit board, cabling, and a network operating system

## Slide 9
A network circuit board called a network card provided the extension of the bus inside the computer to the network. Think of the network card like the on and off ramp from the local streets to the highway.
Cabling is the electronic highway connecting computers with the file server and the early PC networks used the same type of cable that connects your telephone to the telephone net- work. This is called twisted pair.

## Slide 10: Contents
Data Communications
Network
Data Transmission
Communications Media
Network Topology
Local Area Network
Wide Area Network
Organization of Resources
Protocol
Software
Communication Applications

## Slide 11: Data Communications
Send and receive information over communications lines

## Slide 12: Centralized Data Processing
All processing, hardware, software in one central location
Inefficient
Inconvenient

## Slide 13: Distributed Data Processing
Computers at a distance from central computer
Can do some processing on their own
Can access the central computer

## Slide 14: Distributed Data Processing

## Slide 15: Network
Uses communication equipment to connect two or more computers and their resources
PC based
LAN – shares data and resources among users in close proximity
WAN – shares data among users who are geographically distant

## Slide 16: Basic Components
Sending device
Communications link
Receiving device

## Slide 17: Network Design
Transmission
Media
Topology – Physical layout of components
Protocol – Rules governing communication
Distance
  LAN
  WAN
Technology
  Peer-to-peer
  File server
  Client/server

## Slide 18: Data Transmission
Digital lines
  Sends data as distinct pulses
  Need digital line
Analog lines
  Sends a continuous electrical signal in the form of a wave
  Conversion from digital to analog needed
  Telephone lines, coaxial cables, microwave circuits

## Slide 19: Analog Transmission
Alter the carrier wave
Amplitude – height of the wave is increased to represent 1
Frequency – number of times wave repeats during a specific time interval can be increased to represent a 1

## Slide 20: Modem
Modulate
  Convert from digital to analog
Demodulate
  Convert from analog to digital
Speeds up to 56,000 bps (56K)

## Slide 21: Modem
Transmission process
Modulation – Computer digital signals converted to analog
Sent over analog phone line
Demodulation – Analog signal converted back to digital

## Slide 22: Types of Modems
Direct-connect
  External
  Internal
PCMCIA
  Personal Computer Memory Card International Association
  Notebook and laptop computers

## Slide 23: DSL Digital Subscriber Line
Uses conventional telephone lines
Uses multiple frequencies to simulate many modems transmitting at once
No industry standard
  Cost
  Speed
Phone line shared between computer and voice

## Slide 24: Cable Modem
Coaxial cables
Does not interfere with cable TV reception
Up to 10 million bps
Always on
Shared capacity
Security problem

## Slide 25: Cellular Modems
Uses cellular telephone system
Slow speed

## Slide 26: ISDN Integrated Services Digital Network
Digital transmission
Speeds of 128,000 bps
Connect and talk at same time
Need
  Adapter
  Upgraded phone service
Initial costs high
Ongoing monthly fees may be high
Not available in all areas

## Slide 27: Transmission Asynchronous and Synchronous
Sending and receiving devices must work together to communicate

## Slide 28: Asynchronous Transmission
Start/stop transmission
  Start signal
  Group – generally one character
  Stop signal
Low-speed communications

## Slide 29: Synchronous Transmission
Blocks of data transmitted at a time
  Send bit pattern
  Align internal clock of sending / receiving devices
  Send data
  Send error-check bits
More complex
More expensive
Faster transmission

## Slide 30: Duplex Setting
Direction of data flow
Simplex
  One direction
  Television broadcasting
  Arrival/departure screens at airport
Half-duplex
  Either direction, but one way at a time
  CB radio
  Bank deposit sent, confirmation received
Full-duplex
  Both directions at once
  Telephone conversation

## Slide 31: Communications Media
Physical means of transmission
Bandwidth
  Range of frequencies that the medium can carry
  Measure of capacity

## Slide 32: Network Cable
Twisted pair
Coaxial cable
Fiber optic cable
Wireless
  Uses infrared or low-power radio wave transmissions
  No cables
  Easy to set up and reconfigure
  Slower transmission rates
  Small distance between nodes

## Slide 33: Twisted Pair Wire Pair
Inexpensive
Susceptible to electrical interference (noise)
Telephone systems
Physical characteristics
  Requires two conductors
  Twisted around each other to reduce electrical interference
  Plastic sheath
Shielded twisted pair
  Metallic protective sheath
  Reduces noise
  Increases speed

## Slide 34: Coaxial Cable
Higher bandwidth
Less susceptible to noise
Used in cable TC systems
Physical characteristics
  Center conductor wire
  Surrounded by a layer of insulation
  Surrounded by a braided outer conductor
  Encased in a protective sheath

## Slide 35: Fiber Optics
Transmits using light
Higher bandwidth
Less expensive
Immune to electrical noise
More secure – easy to notice an attempt to intercept signal
Physical characterizes
  Glass or plastic fibers
  Very thin (thinner than human hair)
  Material is light

## Slide 36: Microwave Transmission
Line-of-site
High speed
Cost effective
Easy to implement
Weather can cause interference
Physical characteristics
  Data signals sent through atmosphere
  Signals cannot bend of follow curvature of earth
  Relay stations required

## Slide 37: Satellite Transmission
Microwave transmission with a satellite acting as a relay
Long distance
Components
  Earth stations – send and receive signals
  Transponder – satellite
    Receives signal from earth station (uplink)
    Amplifies signal
    Changes the frequency
    Retransmits the data to a receiving earth station (downlink)

## Slide 38: Satellite Transmission

## Slide 39: Combination
Example – East and West coast:
Request made
  Twisted pair in the phone lines on the East Coast
  Microwave and satellite transmission across the country
  Twisted pair in the phone lines on the West coast
Data transferred
  Twisted pair in the phone lines on the West Coast
  Microwave and satellite transmission across the country
  Twisted pair in the phone lines on the East coast

## Slide 40: LAN Local Area Network
Connections over short distances through communications media
Components
PCs
Network cable
NIC

## Slide 41: NIC Network Interface Card
Connects computer to the wiring in the network
Circuitry to handle
  Sending
  Receiving
  Error checking

## Slide 42: Connecting LANs
Bridge – connects networks with similar protocols
Router – directs traffic via best path
IP switches
  Replacing routers
  Less expensive
  Faster
Gateway
  Connects LANs with dissimilar protocols
  Performs protocol conversion

## Slide 43: WAN Wide Area Network
Link computers in geographically distant locations

## Slide 44: Communication Services
Common carriers licensed by FCC (Federal Communications Commission)
Switched / dial-up service
  Temporary connection between 2 points
  Ex: plain old telephone service (POTS)
Dedicated service
  Permanent connection between 2 or more locations
  Ex: Build own circuits, Lease circuits (leased lines)

## Slide 45: High Capacity Digital Lines
T1
  1.54 Mbps
  24 simultaneous voice connections
T3
  28 T1 lines
  43 Mbps
Expensive
High-volume traffic

## Slide 46: Multiplexer
Combines data streams from slow-speed devices into single data stream
Transmits over high-speed circuit (ex T1)
Multiplexer on receiving end needed to restore to component data streams

## Slide 47: Organization of Resources Client/Server and File Server
Clients
Other computers on network
Thin client – no processing
Server
Controls the network
Hard disk holding shared files

## Slide 48: Organization of Resources Client/Server and File Server

## Slide 49: Organization of Resources File Server
Server transmits file to client
Client does own processing

## Slide 50: Organization of Resources Client/Server
How it works
  Client sends request for service to server
  Server fulfills request and send results to client
  Client and server may share processing
Benefits
  Reduces volume of data traffic
  Allows faster response for each client
  Nodes can be less expensive computers

## Slide 51: Organization of Resources Peer-to-Peer
All computers have equal status
Share data and devices as needed
Common with up to 12 computers
Disadvantage – slow transmission

## Slide 52: Organization of Resources Hybrid
Contains elements of various organizations to optimize transmission speed and organizational needs

## Slide 53: File Transfer Software
Download
Receive a file from another computer
Upload
Send a file to another computer

## Slide 54: Terminal Emulation Software
PC imitates a terminal for communication to mainframe
Micro-to-mainframe link

## Slide 55: Office Automation Communication Applications
E-mail
Facsimile (Fax)
Groupware
Teleconferencing
Video conferencing
ATM
Electronic fund transfers
Telecommuting
Online services
The Internet
Electronic data interchange (EDI)

## Slide 56: summary